## Slide 1: WIPER AND WASHER
Aindrila Das
Kumar V B
Niharika B G
Umesh Belle
Vikram G V
Presented by :

## Slide 2: Contents
Introduction
Requirements
Design
System Block diagram
Hardware block diagram
Functional block diagram
Sequential flow chart
CAN Database

## Slide 3
Windscreen wiper is essential for keeping the windscreen sufficiently clean for driver’s visibility specifically for modern high speed vehicles.
Wiper is a device used to remove rain, snow, ice, washer fluid from a vehicle’s front window.
Washer cleans the driver’s side of the windscreen whenever required.
Introduction

## Slide 4
Washer and Headlight washer output
Washer output control should be activated when CAN input(depends on the fluid) is available.
Washer output control should be deactivated when CAN input(depends on the fluid) is not available.
Headlight Washer should be activated when CAN input(depends on the battery) is received.
Headlight Washer should be deactivated when CAN input(depends on the battery) is not received.
Requirements

## Slide 5
Warning Lamp
Hardware warning lamp should be activated when CAN input is not received(i.e the fluid tank is empty).
Hardware warning lamp should be deactivated when CAN input is received (the fluid tank is full).
Warning lamp should be activated when CAN input is not received (i.e there is rain).
Warning lamp should be deactivated when CAN input is received (i.e there is no rain).
Both wiper should be activated when switch 1 and switch 2 are ON.
Rear wiper should be activated when switch 1 is ON and switch 2 is OFF.
Front wiper should be activated when switch 1 is OFF and switch 2 is ON.
Both wiper should be deactivated when switch 1 and switch 2 are OFF.

## Slide 6: System Block Diagram
Wiper and Washer
(Controller)
1.Battery monitoring.
2.Washer fluid tank.
3.Rain sensor.
1.Hardware warning lamp status.
2.Washer output control.
3.Headlight washer.
Faulty message
Front Wiper
Rear Wiper
CAN input
CAN output
H/W output
Wiper input status with TWO switches indicating FOUR states.
H/W input

## Slide 7: Hardware block diagram
PIC18F458
CONTROLLER
Switch 1
Switch 2
LED 1
LED 2
Power supply
CAN transceiver
CAN tool(device)
System
Warning Lamp

## Slide 8: Functional block diagram
Main function
System initialization
CAN initialization
Baud rate
CAN transmit
CAN receiver
Wiper_switches
Switch1
Switch2
Washer output control
Hardware warning lamp status
EEPROM
Headlight Washer

## Slide 9: Sequential flow chart
Start
Enable the peripheral interrupt
PEIE=1
Enable global interrupt
GIE=1
End
System Initialization :

## Slide 10: CAN initialization :
Start
RB3 Enable
RB2 Disable
Enable peripheral interrupt Receive buffer0
Enable peripheral interrupt Priority Receive buffer0
Set baud rate to control register
Set CAN i/o register
End
CAN status
CANSTAT!=80h
Set CANCON in Configuration mode
CANCON=80h
Set Receive Buffer Mode bits to 11
Receive all messages (with errors)
Set CANCON in Normal mode

## Slide 11: CAN transmit :
start
Set CAN to normal mode
Set Standard Identifier Buffer transmit high and low
Enable can request
Data length code
End
Headlight Washer
Washer output control
Hardware warning lamp status

## Slide 12: CAN receive :
Set CAN to normal mode
Data length code
CAN messages
Battery monitoring
Fluid tank
Rain sensor
EEPROM
End
Start
Set receive buffer
Set Standard Identifier Buffer receive high and low

## Slide 13: Interrupt function :
Receive Buffer0 interrupt flag is set
Start
CAN receive()
Faulty message
Warning Lamp is ON
Warning Lamp is OFF
Clear the Receive Buffer0 interrupt flag
End
True
False
False

## Slide 14: EEPROM :
Start
Set the data EEPROM memory and Access program data EEPROM memory
End
Write()
Initialize and enable write cycle
EECON2=0x55
EECON2=0xAA
Store data and address

## Slide 15: Wiper_switch :
Start
Initialize PORTA to 0
PORTBbits.RB1==0
End
True
False
SW1()
RBPU=0//pull up
TRISBbits.RB1=1
LED1 is ON
LED1 is OFF
PORTBbits.RB0==0
True
False
SW2()
RBPU=0//pull up
TRISBbits.RB0=1
LED2 is ON
LED2 is OFF

## Slide 16: Main Function
Start
System Initialization
CAN initialization
CAN transmit
Wiper_switch
Stop

## Slide 17
Node description | Node name | MSG ID | Cycle Time (ms) | MSG Size | Byte 7 | Byte 6 | Byte 5 | Byte 4 | Byte 3 | Byte 2 | Byte 1 | Byte 0
Wiper and Washer | WW | 0x700 | 2000 | 8 |  |  | Warning lamp Activated/Faulty/Not activated: Bit0-Bit1 |  |  |  | Headlight washer output control: ON/OFF/Faulty-Bit0:bit1 | Washer output control: ON/OFF/Faulty-Bit0:bit1
Fluid Tank and Rain monitor | FM | 0x701 | 1000 | 8 |  |  | Bit0-1 :Light rain/Heavy Rain/No rain/Faulty |  | Bit0:Bit1: Normal Voltage/Faulty |  |  | Bit0:Fluid available/Fluid not Available
CAN Database