## Slide 1: WIPER AND WASHER
Aindrila Das
Vikram G V
Niharika Gowda
Umesh Belle
Kumar V B

## Slide 2: Contents
Requirements
Design
  System Block diagram
  Hardware block diagram
  Functional block diagram
  Sequential flow chart
  Implementation
  Testing

## Slide 3: Requirements
Washer and Headlight washer output
Washer output control and should be activated when CAN input(depends on the fluid) is available.
Washer output control should be deactivated when CAN input(depends on the fluid) is not available.
Headlight Washer should be activated when CAN input(depends on the battery) is received.
Headlight Washer should be deactivated when CAN input(depends on the battery) is not received.
Warning Lamp
Hardware warning lamp should be activated when CAN input is not received(i.e the fluid tank is empty).
Hardware warning lamp should be deactivated when CAN input is received (the fluid tank is full).
Warning lamp should be activated when CAN input is not received (i.e there is rain).
Warning lamp should be deactivated when CAN input is received (i.e there is no rain).
Both wiper should be activated when switch 1 and switch 2 are ON.
Rear wiper should be activated when switch 1 is ON and switch 2 is OFF.
Front wiper should be activated when switch 1 is OFF and switch 2 is ON.
Both wiper should be deactivated when switch 1 and switch 2 are OFF.

## Slide 4: System Block Diagram
Wiper and Washer
(Controller)
1. Battery monitoring.
2. Washer fluid tank.
3.Rain sensor.
1.Hardware warning lamp status.
2.Washer output control.
3.Headlight washer.
Faulty message
Front Wiper
Rear Wiper
CAN input
CAN output
H/W output
Wiper input status with TWO switches indicating FOUR states.
H/W input

## Slide 5: Hardware block diagram
PIC18F458
CONTROLLER
Switch 1
Switch 2
LED 1
LED 2
Power supply
CAN transceiver
CAN tool(device)
System

## Slide 6: Functional block diagram
Main function
System initialization
CAN initialization
Baud rate
CAN transmit
CAN receiver
Filter
Mask
Wiper_switches
Switch1
Switch2
Rain sensor
Battery monitoring
Fluid tank
EEPROM

## Slide 7: Sequential flow chart
Start
Enable the peripheral interrupt
PEIE=1
Enable global interrupt
GIE=1
End
System Initialization

## Slide 8: CAN initialization
Start
RB3 enable
RB2 disable
Set CAN configuration
CANCON=80h
Set baud rate to control register
Set CAN i/o register
Set can to normal mode
End
True
CAN status CANSTAT!=00h
False

## Slide 9: CAN transmit
start
Set CAN to normal mode
Set Standard Identifier Buffer transmit high and low
Enable can request
Data length code
End
Rain sensor
Washer fluid tank
Battery monitoring

## Slide 10: CAN receive
Set CAN to normal mode
Set Standard Identifier Buffer receive high and low
Mask
Filter
Data length code
CAN messages
Hardware warning lamp status
Washer output control
Headlight Washer
EEPROM
End
Start
Set receive buffer

## Slide 11: Wiper_switch
Start
Initialize PORTA to 0
SW1=1
SW2=1
SW1=1
SW2=0
SW1=0
SW2=1
SW1=0
SW2=0
End
LATA=0x00
LATA=0x01
LATA=0x02
LATA=0x03
True
True
True
True
False
False
False
False

## Slide 12: EEPROM
Start
Set the data EEPROM memory and config register
Read()
End
Write()
Enable the read cycle and store the data in variable and return
Write address to EEADR
Clear the EEPGD and CFGS control bits
Initialize and enable write cycle
EECON2=0x55
EECON2=0xAA
Store data and address
LATA =Read()

## Slide 13: Main Function
Start
System Initialization
CAN initialization
CAN transmit
CAN receive
Wiper_switch
End